## Slide 1: e-Prelude.com
Technical Data Management
Bills of Materials

## Slide 2: Bills of Materials
Content
  BOM types
  Intermediate Level Creation
  Phantom Items
  Common BOM
  Link Offset
  BOM evolution
  By-products and co-products
  BOM Variants
  Linking components to routing operation

## Slide 3: BOM decimals
For each item, the number of decimals used for the coefficient of its BOM links should be specified
Examples:
  Assembled product: 0 decimal
    Only an integer number of components can be mounted
  chemical combination: 4 decimals
    0.0253 kg for a component

## Slide 4: Which components should be recorded in the BOMs?
Should be recorded in the bills of materials
  all materials and all components
  including waste packaging
Should NOT be recorded in the bills of materials
  components with erratic consumption and/or with a very low cost
    examples: oil, stretch films, tags
  recyclable packaging
    examples: containers, pallets, ...

## Slide 5: BOM types
Engineering BOM
  created by the Product engineering department
  Used during product design phases and development (up to prototyping)
Manufacturing BOM
  created by the Process engineering department
  maintained by the plants
Budget (or Frozen) BOM
  Used as budget reference
  Created by the Frozen Data Creation function (Costing menu)
    Select the date for link selection
    Creates a copy of valid links

## Slide 6: BOM types
An manufactured item can have several BOMs
Select the BOM type in the drop-down list

## Slide 7: Engineering BOM
Structure depends on Product engineering department working methods
Product Breakdown usually by functions
Gradual development
Choices technical performance - manufacturing cost
Transfer to manufacturing

## Slide 8: Manufacturing BOM
Structure depends on the manufacturing steps of a product
Created by the Process engineering department when it enters the routings
It must be verified that, at the lowest level, all the components entered by the Product engineering department are found in the manufacturing BOM

## Slide 9: BOM Links
New fields

## Slide 10: Creating an intermediate level
FG
C1
C2
C3
FG
S/A
C3
C1
C2
Advantages of creating an intermediate level: 1 – easier description of planning rules 2 – managing an inventory is easier than managing a WIP
3 – assembly which can be common to several parent items
Disadvantages: have to manage an additional item
?

## Slide 11: Rules for creating a BOM level
Rules:
  1 - minimize the number of levels
  2 - create a sub-assembly only if inventory can exist
  3 - create a sub-assembly if there is a break in the production stream
  4 - create a sub-assembly if there is an independent demand (external requirements)
Practice:
  Do not create a BOM level when the assembly operation is carried out as a result of the preceding operation (in the stream)
  Create a BOM level at each declared manufacturing step

## Slide 12: Effects of an intermediate level
FG
SA2
SA1
P1
P3
P2
FG
P1
P3
P2
Allows to grouper requirements for common sub-assemblies
Receipt-Issue Transactions
Longer manufacturing cycle
Manufacturing Cycle
Manufacturing Cycle
“Rake” BOM
(single level)

## Slide 13: Phantom Items
Definition
  Non-storable items (ephemeral existence)
  Have a BOM
  Do not have a routing
  Cannot support sales forecast, Customer orders, Work orders…
Examples of use
  Structuring complex BOMs
  Grouping of components common to several BOMs
  Creation of common BOMs

## Slide 14: Common BOM
Principle:
  Two products having exactly the same components can and must use a common BOM
  Any change will concern both products
  Example:
  Two parts, left and right are made with one kg of material M
  A change (ex: using only 0,9 kg of M) will automatically concern both parts
  Practice:
  Create a phantom item to support the common BOM

## Slide 15: Common BOM
FG1
C1
C2
C3
FG2
C1
C2
C3
Phantom
C1
C2
C3
FG1
Phantom
FG2
Phantom

## Slide 16: Packaging BOM
Packaging is indicated in a link with the finished product
The coefficient represents the "fraction" of packaging used by a finished product
Example: if you put 12 parts in a carton, the coefficient will be 1/12 (that is 0.0833)

## Slide 17: Packaging BOM
Quantity
of parent items
in the quantity of components specified by the coefficient

## Slide 18: Link Offset
Object:
  modify the requirement date calculated from the item lead time for some components in the BOM
Negative Offset
  Makes it possible to introduce a safety lead time for a particularly sensitive component
Positive Offset
  Allows to indicate that a component if not required at the release date but at the end of the process (example: packaging)
Specified in days

## Slide 19: Link Offset
Item Lead Time
Work Order Due Date
Work Order Release Date
Normal required component date (offset 0)
Negative offset
Positive offset
Required component date with a negative offset
Required component date of a component used at the end of the process
Another solution: Attaching components at each routing operation

## Slide 20: BOMs changes over time
Object:
  Plan for future product developments (Engineering changes)
  Find the composition of a product manufactured in the past (After sales)
Practice:
  Changes are identified by
    Validity start and end dates in product structure record
    Serial numbers or Engineering change notice (not supported by e-Prelude)

## Slide 21: BOMs changes over time
Changes are identifies by validity dates on product structure records Used in the MRP process at release date
FG
C1
C21
C22
Link valid till March 21st
Link valid from March 22nd
FG
C1
C21
FG
C1
C22
BOM till March 21st
BOM from March 22nd

## Slide 22: Mass Replacement
A component can be automatically replaced by another
  In all its where-used parent items
  From an effective date
Example:
  Replacing a purchased component

## Slide 23: Options and Variants
Definition:
  an option, it is one or several additional components
  a variant, it is one or several different components
Object:
  Describe slightly different products without having to completely rewrite the BOMs

## Slide 24: Options and Variants
Method base + options
  Phantom items grouping common components
Method base + variance
  Create as many finished products as combinations of options / variants
  These methods can only be used at the higher BOM level
Link selection
  All the possible links are entered Valid links are selected using the value of an attribute
  (not implemented in e-Prelude)

## Slide 25: Method Base + options
FG220
FG110
Base
Base
Conv220
Conv110
All common components
FG optional component
FG optional component

## Slide 26: Method Base + variance
FG220
FG110
C1
Conv220
Conv110
Base item variant
Base item
C2
FG220
Conv220
C1
Conv220
C2
(-1)
(+1)

## Slide 27: Selection of records
FG
FG
Conv220
Conv110
FG
Generic item
C1
Conv220
C2
Conv110
On each record: a selection attribute
Attr
FG-220
220
110
FG-110
Variant 220
Variant 110

## Slide 28: By-product or co-product
Object:
  Describe the fact that a by-product is created when the main product is manufactured
Method:
  crate the by-product as a component
  Enter a negative coefficient on the record
Example:
Produit
Material
By-product
Coef. : 2,5
Coef. : -1
When planning 1000 products - a need for 2500 is created on the material - a negative requirement of 1000 is created on the by-product which gives rise to an inventory receipt

## Slide 29: BOM Variants
A parent item has necessarily at least one Manufacturing BOM (M)
  Used in the MRP process
You can create one or more variants of M BOMs
  Can be used to update requirements of a planned order
  Select a name in the variant list table (Engineering menu)
  A BOM variant is linked to a routing
Examples
  A component is purchased instead of being manufactured
  Temporary transfer of work load to a contractor

## Slide 30: BOM Variants
Method
  Create BOM Variant Table (menu Engineering, option BOM Variant Table)
  Create for each variant, the item BOM (Bill of Materials Maintenance page)
  Assign a BOM variant to Item routings (Item Maintenance page, Routing grid)
The planning process will take into account the item release routing and the BOM variant attached

## Slide 31: BOM Variant Selection

## Slide 32: Specifying BOM Variants
For each routing, it is possible to attach a BOM variant

## Slide 33: BOM Variants (another solution)
Create Phantom items as parent items
Create BOM variants for each Phantom item
Attach one of these phantom items to the manufactured item
  permanently (BOM of manufactured item)
  temporarily (for one work order)

## Slide 34: BOM Variants (another solution)
Manufactured item
Variant 1
Variant 2
C1
C2
C3
A1
C2
C’3
Phantoms

## Slide 35: Attaching components to each operation
Op. 010
Op. 020
Op. 030
Op. 040
Manufactured Item
Material 1
Material 2
S / A
It is indicated to which routing operation the component is used
This information is used for
Planning components requirements
Components backflush at each operation
Manufacturing routing

## Slide 36: Attaching components to each operation
Nouvelle zone

## Slide 37: Attaching components to each operation
Op. 010
Op. 020
Op. 030
Op. 040
WO Due Date
WO Release Date
Due date
for components
attached
to operation 040
Due date
for components
attached
to operation 030
Due date
for components
attached
to operation 020
Due date
for components
attached
to operation 010
and components
Not attached
to any operation
Components Due Dates
are calculated while scheduling the Work Order

## Slide 38: Effects on Production Cycle
FG
S/A2
S/A1
P1
P3
P2
FG
S/A2
S/A1
P1
P3
P2
Production Cycle
Production Cycle