## Slide 1: e-Prelude.com
Technical Data Management
Items

## Slide 2: Item Management
Content
  Codification
  Item attributes
  Stock unit of measure and purchasing unit of measure
  Phantom Items
  Non stocked items

## Slide 3: Which Items should be recorded?
Finished goods
Sub-assembly or intermediate products
  Manufactured or sub-contracted
Purchased goods
  Raw materials et components
Trade goods
  Purchased and sold without any transformation
Packaging
  boxes, ...

## Slide 4: Items involved
Purchased goods
  Raw materials and components
Sub-assemblies
  manufactured or sub-contracted
Finished goods
  Trade goods
  Purchased and sold
Packaging
  boxes, ...

## Slide 5: Item codification
Mnemonic Codification
  Advantage: easy to identify the item
  Disadvantage: required to create long, complex and difficult to maintain codes
  Often involves alpha codes
Example
  SWHC0530 (wood screw, countersunk head, diameter 5 mm, length 30 mm)

## Slide 6: Item codification
Arbitrary Codification (numeric)
  Advantage: short codes, easy to enter, no classification problem
  Disadvantage: requires to keep lists to find the item
Example
  31822045

## Slide 7: Item codification
Mnemonic Root (family, nature or category) + a chronological sequence
Advantage: it is easy to identify the item nature
Example
T FFF nnnn
Type
Family
Sequence Number
Examples of types:
1 : Raw materials, 2 : Purchased components, 3 : Consumables
4 : Sub-contracted items, 5 : Manufactured items, 6 : Phantom items, ...

## Slide 8: Item Maintenance
Additionnal
Information fields

## Slide 9: Item Attribute Tables
Engineering Menu
  Item Status
  Unit of measure
  Item Category
  Item Nature
  ABC Class
  Planner
Logistics Menu
  Inventory Status
  Warehouse

## Slide 10: Attribute Table Maintenance
Enter the code then the description. Validate with OK
Select the table to update :
Note: Accounting information are entered in the Item Category Table

## Slide 11: Item status
Characterize item during its life cycle
Activated
Prototype
Pre-serie
Accepted
Serie
Fin de vie
Obsolete
Desactiv.
Each status can correspond to a number of locks
Life stages are reversible
Some life stages can be skipped
Item status are not managed by e-Prelude

## Slide 12: Units of measure
The unit of measurement describes the unit in which the item is managed within the company
  examples: part, pound, meter, …
We also specify the number of decimals in the stock management according to the desired precision
  0 : 25 kg
  3 : 1.253 kg

## Slide 13: Warehouses
Physical Warehouses
  Geographical locations in which items can be stored
  examples:
    RM: Raw material warehouse
    SF: Semi-finished products warehouse
    FG: Finished goods warehouse
Inventory reports per warehouse
Access: Logistics Menu, Warehouse Table Maintenance Option

## Slide 14: Warehouse available for MRP or not
Specifies if the inventories in this warehouse can be taken into account by the MRP function
Indicates the warehouse capacity

## Slide 15: Item categories and natures
Categories
  Grouping of items by commercial families
  linked to general ledger
Natures
  Grouping on physical or technical characteristics
  ex: plastic parts, screws...

## Slide 16: ABC classes
Characterize the economic importance of each item
Classification according to consumption value
Relations to Reorder Policy

## Slide 17: Planners / Buyers
Agent in charge of managing the supply of the item
Purchased Item: it is the buyer
Manufactured Item: it is the planner
Specific reports per buyer / planner

## Slide 18: Inventory status
The notion of inventory status is described in the Inventory Management presentation
For each item, it is the default status for inventory transactions
  example: a purchased item has to be inspected before it can be used by the workshop -> default status : INSP

## Slide 19: Item weight
Item weight in its unit of measure
Allows to plan packaging and transportation
Automatic calculation of the weight of a parent item with the weight of its components by the cost roll-up function

## Slide 20: Item Volume
The item volume is described as the number of units which can be stored on a pallet
Allows to calculate
  The volume of flows of goods (in number of pallets to ship and to receive)
  The warehouse capacity utilization

## Slide 21: Stocking unit and purchasing unit
The unit in which a product is purchased may be different from the unit in which the product is managed internally
  example: 10 m sheet strips are purchased and managed in meters
  We specify a conversion coefficient between units (ex: 10)
Different suppliers of the same item may have different purchasing units

## Slide 22: Stock unit and purchasing unit
Stock unit of measure
(item window)
Purchasing unit and
conversion coefficient

## Slide 23: Packaging
This is the vendor's multiple sales unit
  example: Pallets of 8 drums
  We will have to order a multiple of the packaging quantity

## Slide 24: Phantom Items
Allows to structure the BOMs
Allows to create common BOMs
Can not give rise to work orders and cannot be stored
Are "transparent" in the requirements calculation procedure
They will be treated in the slideshow on the BOM management

## Slide 25: Non-stocked Items
Articles which cannot be physically stored
Do not have BOM or manufacturing routing
Can be used in BOMs to indicate material or intangible elements used in the item valuation
  examples: oil, rags, paper, screws…
Can also be used to invoice services or labor
  Hours of maintenance
  Packaging
  Not to be confused with the Item reorder policy "Not managed"

## Slide 26: Item Management Parameters
Will be described in the presentation about production planning