## Slide 1: e-Prelude.com
Tour - session 6
Production Planning

## Slide 2: Production Planning Purpose
Satisfy customer orders
Place purchase orders to vendors
Insure a high capacity utilization
Aim to a minimum inventory level
Provide a work plan to the workshops

## Slide 3: Finished good Demand
The planning process starts from
  Sales orders
    Firm orders
    Shipment schedules
  Sales forecast
    Made by the manufacturer
  Inventory look up
    For items made to stock if the on-hand quantity is lower than the order point

## Slide 4: Calculation of quantities to make and to source
General principle: Materials Requirements Planning (MRP)
Alternate method:
  Managing inventories
Notes: La gestion sur stock de type “mini-maxi” est très peu utilsée sauf pour les articles de faible valeur comme les consommables
ex : film étirables, huile de coupe ...

## Slide 5: MRP Principle
It starts with end-items (level 0) to generate quantities of immediate components (level 1) using the BOM. These are called gross requirements
By taking into account the existing inventories, it computes the net requirements at this level = Gross requirements – Inventory on hand + Inventory desired level (safety stock)
Future requirements are eventually regrouped (lot sizing)
Similarly, all other levels are analyzed
To position the requirements in time, it takes into account the production/procurement lead times of the items

## Slide 6
Level 0 : Finished goods
Gross Requirements =
Orders/Forecasts
FG Inventory
and assembly WIP
Finished Good Net Requirements
Finished Good Assembly Orders
Level 1 : Sub-assemblies
Finished Good BOM
Sub-assembly Gross Requirements
Sub-assembly inventory
and manufacturing WIP
Sub-assembly net requirements
Sub-assembly Manufacturing Orders
Level 2 : Parts
Sub-assembly BOM
Part Gross Requirements
Part Inventory
and fabrication WIP
Part Net Requirements
Part Fabrication orders
Part BOM
Level 3 : Materials
Material Gross Requirements
Material Inventory
and open purchase orders
Material Net Requirements
Purchase orders
Notes: La procédure de planification se déroulera en deux phases :
- niveau MPS (produits finis)
- validation manuelle des ordres proposés
- niveau MRP (tous les autres articles)
- validation manuelle des ordres proposés

## Slide 7: Taking into account the production lead time
  To determine the release dates (for the parts to be produced) and those of the purchase orders (for the parts to be purchased), one must take into account the lead time required to obtain the parts (expressed in days).
  For purchased parts, the lead time is the Delivery Lead Time of the supplier
  For the parts produced internally, it is the time required to complete all the production stages of a batch of products. This time is defined in the routings.
Parent Item
Requirement Date
Parent Item Release Date
Manufacturing Lead Time
Date of component requirements

## Slide 8: Taking into account the procurement lead time (for purchased items)
Material requirement date
Date of purchasing order issue
Procurement lead time
Specifies in days on the item Reorder Policy page

## Slide 9: Lot-Sizing Decisions
MRP determines net requirements but tries to optimize orders
Main Techniques:
  Lot for lot
  Economic Order Quantity (EOQ)
  Part Period Balancing
  Algorithms or heuristics
Disadvantages : they increase the levels of inventories

## Slide 10: Lot sizing decisions
Goal:
  Avoid creating too many work or requisition orders in a short period of time
  Thus reduce the number of production orders releases or purchase orders
    which generate fixes costs (clerical work, changeover time, transportation, …)
but...
  creation of inventory
    (because a requirement is anticipated)

## Slide 11: Item Management Parameters
1 - Select the Reorder policy
2 - Select the lot sizing rule
3- Specify the production lead time
Access: Planning menu, Item Reorder Policy option
4- Validate

## Slide 12: A production process
Sub-assembly
SA 1
Material
X
Material
Y
Part
A
Part
B
Finished good
Sub-assembly
SA 2
Sub-assembly
SA 3
Routing
Routing
Routing
Notes: La gamme décrit le processus pour passer d’un niveau de la nomenclature au niveau supérieur

## Slide 13: Production planning steps
Requirements
Planned Work Orders
Manufactured items
MRP calculation
Conversion
Firm Work Orders
Order release
Open Work Orders
Planned requisition orders
Purchased items
Conversion
Firm requisition orders
Purchase order entry
Purchase Orders
Execution
Closed Work Orders
Receipt
Closed Purchase Orders

## Slide 14: Successive Work Order status
Planned WO
Firm WO
Open WO
Closed WO

## Slide 15: Work order status depending on the time horizon
Planned WO
Firm WO
Open WO
Closed WO
MRP Calculation end date
WO Conversion end date
WO Release end date
Current date
time

## Slide 16: A calendar
Mo
Tu
We
Th
Fr
Sa
Su
Mo
Tu
We
Th
Fr
Sa
Su
Mo
Tu
We
Th
Fr
Sa
Su
The plant calendar defines working days
Requirements offsets are calculated on working days
Example:
  There is a requirement for item A with a lead time of 6 days for Wednesday of week 3
  The release date is calculated by moving backward on the calendar of the number of days of the lead time
Week 1
Week 2
Week 3
6 days
Requirement
Release

## Slide 17: Materials Requirements Planning
Items are processed by increasing level order
Specify a calculation end date to avoid generating orders for far demands
Access: Planning menu, Material Requirements Planning option

## Slide 18: Planned Work Order List
Access: Planning menu, Planned Work Order List option

## Slide 19: The Planned Work Order window
Access: Planning menu, Planned Work Order Maintenance option

## Slide 20: Item Master Schedule
Planned orders appear in the Master Schedule
Inventory Profile is updated
Access: Planning menu, Master Schedules option

## Slide 21: Scheduling and capacity utilization
WO are scheduled using infinite capacity loading
  One after the previous without taking into account the number of available machines on the work center
Operations are placed with times calculated from the routings on work center time slots (calendar)
  forward (starting from the release date)
  backward (starting from the due date)
Work loads are cumulated on each time slot

## Slide 22: Work center schedules
Using the calendar, determination of working time slots for each work center
8h
8h
8h
8h
8h
8h
8h
8h
8h
8h
WC 1
WC 2
Mo 8:00
Tu 8:00
We 8:00
Th 8:00
Fr 8:00

## Slide 23: Scheduling of a Work Order Example
Release date: Monday
Due date: Friday (must be finished on Thursday night)
Operation 010 on WC 1, duration 10 hours (setup time + run time) + 3 hours for transfer
Operation 020 on WC 2, duration 12 hours (setup time + run time) + 3 hours for transfer

## Slide 24: Forward scheduling
8h
8h
8h
8h
8h
8h
8h
8h
8h
8h
WC 1
WC 2
Mo 8:00
Tu 8:00
We 8:00
Th 8:00
Fr 8:00
Op. 010
Release date
Due date
10h
3h
3h
Op. 020
12h
Earliest end date
Slack: 4h

## Slide 25: Backward scheduling
8h
8h
8h
8h
8h
8h
8h
8h
8h
8h
WC 1
WC 2
Mo 8:00
Tu 8:00
We 8:00
Th 8:00
Fr 8:00
Release date
Due date
10h
Op. 020
3h
12h
Latest start date
Slack: 4h
Op. 010
3h

## Slide 26: Infinite Capacity Scheduling
Access: Planning menu, Infinite Capacity Scheduling option
Specify a calculation end date to avoid useless calculations

## Slide 27: Infinite Capacity Scheduling Chart
Access: Planning menu, Scheduling Chart option

## Slide 28: Infinite Capacity Schedule Dates
Access: Planning menu, Planned Work Order Maintenance option
Scheduling dates are calculated

## Slide 29: Work Order Slack Analysis
Access: Planning menu, Planned Work Order Slacks option

## Slide 30: Capacity Utilization
8h
8h
8h
8h
8h
WC 1
Mo 8:00
Tu 8:00
We 8:00
Th 8:00
Fr 8:00
On each time slot, work loads originating from WO are cumulated
For Forward and Backward schedules
WO 1
4h
6h
WO 2
4h
8h
2h
WO 3
2h
8h
5h
4h
Work Load
12h
16h
7h

## Slide 31: Work Load Table
Access: Planning menu, Scheduling Chart option

## Slide 32: Work Capacity Utilization Summary
Access: Planning menu, Resource Capacity Utilization Summary option

## Slide 33: Workload Chart
Access: Planning menu, Workload Chart option

## Slide 34: End of session 6